# ARCHITECT/ENGINEER SHORT FORM SPECIFICATION

To specify any of the formliners by Fitzgerald Formliners, please include the following language in your architectural specifications:

All concrete surfaces designated in the engineering plans or specifications as "textured architectural concrete" shall be formed using Fitzgerald Formliners Pattern No. ______________ as manufactured by Fitzgerald Formliners, 1500 E. Chestnut Avenue, Santa Ana, CA  92701, phone 714-547-6710.  No substitutions will be allowed without prior written approval from the project architect or engineer.  Any substitute product must be submitted two weeks prior to the bid date.

# SUBMITTAL

- Sample Panel: Within thirty days of receiving contract, the Prime Contractor is required to submit a 24” x 24” sample of the formliner pattern.  Architect/Engineer and Owner require approval of sample panel.

- Shop Drawings:  Plan, elevation, and details showing overall pattern, joint locations, form tie locations, end locations and other special conditions.

- Samples: Form ties, samples, and description, showing method of break-back when forms are removed.

# MOCKUP

Build on site 30 days prior to commencing work, using same materials, methods and work force that will be used for the project.  Architect/Engineer and Owner will determine specific requirements and location, and whether mockup shall be incorporated as part of the final project.

- Size: 16 Sq. Ft. or larger if needed to adequately illustrate the pattern and texture selected.

- Include an area to demonstrate formliner butt joint and, if appropriate continuation of pattern through construction joint.

# CONSTRUCTION

Prepare, install, and finish in accordance with current release of manufacturer’s Application Guideline for the particular type of formliner used.